## Slide 1
D Y E M A N A G E M E N T G R O U P, I N C.
TRC Transportation Conference & Equipment Expo
August 15, 2019
NCHRP 13-04 Optimal Fleet Replacement Cycles Tool Implementation Support

## Slide 2: Outline
Project Purpose and Importance of Effective Fleet Replacement
Project Outputs
Life Cycle Cost Analysis
Replacement Decision Process
Replacement Factors
Excel-Based Tool Demonstration
Future Work
Notes: Focus on “this was completed as part of NCHRP project guidelines”

## Slide 3: NCHRP Project Purpose
Develop rational replacement processes based on optimal life cycles
  Develop processes and tools to assist the replacement planning process
  Assist equipment managers and administrators with the task of equipment replacement
Notes: Remove. Simply note it was completed under NCHRP guidelines

## Slide 4: Benefits of Effective Fleet Replacement
Other benefits include:
Better equipment leads to
  Operational efficiencies
  Cost savings
Safety
Employee morale
  Public perception and image
Notes: - Equipment is an asset vital to agency’s mission
  Necessary to develop and implement a systematic approach to support effective fleet replacement decisions
- Equipment replacement merits the attention of dedicated resources within the fleet management organization
- Optimal fleet replacement results in reduced costs of equipment ownership and operation
Morale? Public perception if a citizen sees and old fleet
Combine with slide 4.

## Slide 5: ArDOT Project Objectives
Evaluate current fleet replacement cycles
Update existing replacement schedules
Prioritize specific equipment units for replacement
Notes: ArDOT has replacement cycles but they don’t know if they are “optimal”

## Slide 6: Life Cycle Cost Analysis
Life-Cycle Cost Analysis
Notes: Life-Cycle Cost Analysis (LCCA) is the industry best practice for determining optimal life cycles.
This is a stylized graph representing LCCA
In real-world application, the curves are rarely smooth but rather erratic; reflecting how maintenance and repairs are performed on equipment from year to year.
Optimal replacement is seldom a single point in time but rather a window of time.
Discuss make-up of curves – ownership and operating
Important note: Looking at an individual unit of equipment, optimal life cannot be determined until after the fact. We’ll demonstrate this later.

## Slide 7: Replacement Factors
Maintenance, repair, and fuel costs
Age
Condition and criticality
Depreciation
Replacement
Downtime
Obsolescence
Utilization
Overhead costs
Notes: These are the factors typically found in LCCA.
We will discuss each in more detail. However, I’ll focus on those items listed in BOLD.
Mention downtime and that it is important to track but many agencies do not.
To be discussed more later, the tool uses default values for selected factors based on analysis of real world data from several DOT sources

## Slide 8: Depreciation
Not accounting depreciation
Based on actual salvage value of unit
Average salvage values from DOT data
Tool depreciation curves based on utilization – not age
Notes: Not accounting depreciation.
Based depreciation on utilization. Accounting departments base depreciation on age (straight line or double-declining method). 2 vehicles: Both are 8 years old. 1 has 100,000 miles, 1 has 150,000 miles. The accounting depreciation would value those the same. We look at the extra 50,000 miles of utilization.
In our experience, we find that buyers are interested in DOT equipment because, in general, they are maintained very well.

## Slide 9: Typical Depreciation Curve
Example depreciation schedule, ½-ton pickups
Depreciation Schedule |  |  |  |  |  |  | 
Miles | 10,000 | 20,000 | 30,000 | 40,000 | 50,000 | 60,000 | 80,000
Accumulated Depreciation | 15% | 24% | 32% | 40% | 47% | 53% | 59%
Notes: We analyzed equipment resale values from several DOTs to come up with default depreciation curves which are built into the tool.
Analyzing actual ArDOT resale data
Depreciation curves can and should be customized by the user.
Some fleet agencies receive no returns on equipment sales because the sale proceeds are returned to a general fund and not to the fleet agency. The tool accounts for this by allowing the agency to override the default values and to set salvage values at zero at a selected age or utilization level.

## Slide 10: Ownership Cost Component (Depreciation) of LCCA Example
Equipment Type | 1/2-ton pickup | 
LTD Utilization | 45,500 miles | 
Replacement Cost | $25,000 | 
Accumulated Depreciation | = | (Accum. Depr. %) * Replacement Value
 |  | 43.5% * $25,000 = $10,875
The LCCA ownership cost component is based on LTD cost per mile |  | 
LTD cost per mile = $10,875/45,500 miles = $0.24/mile |  | 
Notes: When setting up the optimization tool for the first time, you can use the default depreciation values or customize them to your agency’s needs
Note the 43.5% comes from the depreciation schedule displayed on previous slide.
More detail on how to develop these depreciation schedule in the Guide

## Slide 11: Maintenance and Repair Costs
Preventive Maintenance
Scheduled and unscheduled repairs
Accident repairs and body work
Rebuilds and overhauls
Notes: Major component of the total cost to own and operate equipment
Typically accounts for up to 40 percent of the unit’s total cost over its life
Initial outfitting should be charged to the original purchase price (capital)
Some people think we should not include accident repairs. Example: vehicle in a minor accident. Shop could repair more than is necessary to repair that dent. Reporting headache to pull out the repairs for that accident only.
Users would need to be able to distinguish an accident repair from a regular repair. Accidents will typically be a very small percentage of all repair costs.
There is a repair versus replace analysis project coming from NCHRP soon. This is a separate decision than LCCA. If an agency chooses to rebuild a piece of equipment, this should be included in the M&R costs. If there is a significant rebuild, an agency could also choose to remove that specific piece of equipment from the class analysis and run unit-level LCCA for that specific piece of equipment.

## Slide 12: Condition and Mission Criticality
Engine
Body
Electrical
Transmission
Steering/ Suspension
Frame
Notes: 6 components
Tool utilizes the condition score and LTD cost to determine replacement priorities
Not monetary factors in LCCA
Body, engine, transmission, steering/suspension, and electrical components to assessment.
Weights customizable to each agency
More on this later in the presentation
Does not impact the optimal replacement cycle. It is part of the replacement decision-making process. See #2 and 3 of the project objectives.
This aligns with the performance-based approach to managing assets

## Slide 13: Overhead
Historically, mechanic hourly rates have not fully recognized overhead
Overhead for warehouse, non-chargeable mechanic time -- mechanic training, shop clean-up
True operating costs are understated without fully-loaded mechanic hourly rates
Tool has feature to include overhead
Notes: We were not able to get into the financial and payroll data of DOTs; however, from discussions we found that the mechanic hourly rates used to determine operating costs are likely significantly lower than they actually are.
This would tend to make LCCA optimal life calculations to be longer than they should be.
Therefore, we provided a feature in the tool to allow users to account for fully loaded overhead on mechanic hourly rates.
Mechanic/shop overhead can be significant today. Computers, software, diagnostic equipment, etc. When a mechanic is working on a piece of equipment, that is chargeable time. When he is cleaning, training, having meetings, etc. is still a cost that needs to be added on to his hourly rate.
We suggest agencies perform a review of their current overhead rates to ensure they are capturing the full accounting of mechanic overhead. One agency (WV Turnpike) was charging mechanics out at $35/hour. Following an internal analysis, they found they should be charging them out at $53/hour.
The tool comes with default overhead rates. These should also be tailored to each agency.

## Slide 14: Replacement Cost
Utilized in two ways:
  To calculate depreciation in LCCA
  To project long-range replacement budget needs
Should include the purchase price + cost of outfitting the unit prior to deployment
Notes: Replacement costs should be updated annually
Tool uses the average replacement cost for all units in a class
Should include the purchase price + the cost of upfitting the equipment unit prior to deployment.
May also choose to use a replacement cost that represents the majority of the units within a class
Decision made based on DOT data and testing. Decided everything is based on constant year dollars. Decided not to use original purchase cost, not replacement cost. Class-level LCCA has vehicles from 1-15 years old in the class with various original purchase prices. 20 that are 1 year old, 2 that are 2 year old, etc. Did not make sense to use original purchase cost due to variation in original purchase price.
Replacement cost is entered in the Configuration File.

## Slide 15: Making Replacement Decisions is a Process
Notes: Equipment replacement involves art and science
Equipment replacement decisions are much like any other asset management approach.
We found that data cleanup is VERY important in the process, and it may actually be the most time-consuming task in the process.
LCCA can determine optimal life cycles.
But knowing when to replace equipment and making replacement decisions are two different exercises.
Equipment condition and mission criticality are not monetary factors in LCCA, but they are important in the decision making process

## Slide 16: Excel-Based Tool
Determine optimal life cycles for each equipment class
Perform LCCA on individual equipment units
Identify candidate replacement needs
Prioritize equipment replacement units
Develop a 5-year replacement needs budget
Analyze the cost consequences of various replacement cycles
Notes: The tool has 6 main functions, as shown in the slide
I have several more slides on the presentation but these are mainly for reference for folks later.
I think we’ll be best served to begin the tool demonstration and discuss these features and functionality as we step through that process.

## Slide 17: Class-Level LCCA
Looks at all units in a specific equipment class
LTD cost per mile calculated for each of the cost components
Total cost per mile is obtained by totaling maintenance, fuel, downtime, operating costs
Tool develops a trend line to model the total cost curve

## Slide 18: ArDOT Classes for Analysis
Tool comes preloaded with 40 major equipment classes
Preliminary analysis for ArDOT focuses on 11 classes
Analyzing multiple codes within the major classes
Notes: Dump trucks, pickups, motor graders, mowing equipment, truck mounted units, asphalt equipment, sweepers, rollers, backhoe loaders, wheel tractors, loaders
Codes within classes example = 6, 10, and 12 Cu Yd.

## Slide 19: Identify Replacement Candidates
Tool identifies potential replacements that:
  Are past their replacement targets (miles or hours)
  Have high costs (>25 percent) compared to the class average
Only candidates for replacement
Each unit should be evaluated individually

## Slide 20: Perform Condition Assessments
Provides insight on individual units
Notes: Reiterate that LOS/performance-based budgeting utilizes asset condition. Same approach should be applied to equipment replacement.
Again, can be incorporated into the annual PM or inspection process.
Weights for each component (body, engine, etc.) can be tailored to the agency
Not currently linked to the other spreadsheets in the tool but is a recommended enhancement

## Slide 21: Prioritize Replacement Units
Tool determines priority ranking based on unit’s LTD cost and condition score
Priority report will only show units with condition scores have been entered
Default weighting of 40/60 percent to cost and condition
Notes: - 40/60 weight of cost and condition can be tailored to specific agency in the Configuration File as shown in the screen shot.

## Slide 22: Unit-Level LCCA
Analyzes cost performance of individual equipment units
Requires annual data by unit
Consider other factors (beyond cost) such as condition and mission criticality
Notes: - Unit-level LCCA must have cost history (miles/hours, maintenance and operating costs, downtime) for each unit’s life. If annual cost data is not available, the optimization tool will not produce reliable LCCA results.

## Slide 23: Determine Replacement Program
Tool informs decision-makers
Guidelines for final decision making:
  Priority ranking as a starting point
  Utilize condition assessments to identify units in the best condition
  Unit-level LCCA to identify trends of individual units
  Consider cost, condition, and other objective factors in final decision
Notes: If sufficient funds are available, the decision-making process would be easy
However, equipment replacement decisions are made in a world of constrained resources.
No defined process for making the final replacement decision. This is where the “art” comes in.

## Slide 24: Develop 5-Year Plan and Budget
Planning tool to communicate future budget needs
5-Year Plan shows which year a unit is projected for replacement and calculates the total budget for each year
Notes: We talk a lot in asset management about communicating needs to decision-makers
MAP-21 mandates a 5-year planning horizon, Long Range Plans, etc.

## Slide 25: Analyze Cost Consequences
Optional step
Helps fleet managers develop a business case for funding levels
Tool analyzes annual cost of various replacement cycle scenarios
Compares impacts of “optimal” versus “other” replacement cycles
Notes: Provides helpful information that managers can use to make a business case
We use similar tools/data in other asset management efforts. “$XXX,XXX,XXX to achieve all our target LOS. If we get $XX,XXX,XXX this is the LOS you can expect.”

## Slide 26: Future Work and Enhancements
Finalize analysis based on detailed ArDOT cost data
Finalize recommendations
Train users on the tool
Build tool in more robust software
Notes: Begin tracking downtime
Determine true mechanic hourly rate
The tool could be improved by building in a more robust software application.
  Currently beyond the scope of the project
  Access or web-based
  Would enable more user-specific configuration
  Reduce time it takes to develop report
Develop data validation feature
  Automatically checks agency data and alerts users if values are outside typical ranges
We need to determine how to effectively (considering real world operating conditions) track downtime.
Implementing effective equipment replacement processes requires the commitment of resources within the fleet agency. This could merit a full-time position dedicated to equipment asset management (just as pavements and bridges).
Making equipment replacement decisions combines art and science. Training and repeated use of the tool and processes will be required to become proficient.
Tool currently looks at age to determine your 5-year plan. Would develop functionality to forecast when a piece of equipment would hit the utilization (miles/hours) target based on current annual usage. Rather than age solely.

## Slide 27
601 108th Avenue NE Suite 1900  Bellevue, WA 98004-5500 T: (425) 637-8010 F: (425) 637-8020  www.dyemanagement.com
DMG Contact
jholabaugh@dyemanagement.com
DYE MANAGEMENT GROUP, INC.